## Slide 1: Design Project Title : Autonomous Robot Navigation Using Reinforcement Learning
Rigvita Sharma
2016A7PS0067P
Shruti Sharma
2016ABPS0833P
Submitted To: Dr J L Raheja

## Slide 2: Introduction
Here we have worked on the development of a object detection algorithm for robot navigation using reinforcement learning.
It uses D3QN to train the turtlebot in simulated environment Gazebo.

## Slide 3: OBJECTIVE
Conversion of RGB-D images into Point Cloud Data.
Develop an object detection algorithm using ROS-PCL
Develop a dataset of depth PCD images using Kinect v2 for assisting in the implementation of a given algorithm on an actual robot.
Developing an obstacle avoidance algorithm using reinforcement learning.

## Slide 4: Related Work
Towards Monocular Vision based Obstacle Avoidance through Deep Reinforcement Learning
Sim-to-Real: Learning Agile Locomotion For Quadruped Robots
Automatic Robot Navigation using Robot Navigation - Master Thesis

## Slide 5: Softwares/Libraries used
ROS Kinetic
Gazebo 7
Tensorflow
Python 2
Opencv
Open3d
PCL
Kinect Studio
C++

## Slide 6: Conversion into Point Cloud Data
RGB-D dataset
RGB-D dataset
Open-3D
Point Cloud Data
Code Snippet Used:
pcd = create_point_cloud_from_rgbd_image(rgbd_image, PinholeCameraIntrinsic(PinholeCameraIntrinsicParameters.PrimeSenseDefault))
pcd.transform([[1, 0, 0, 0], [0, -1, 0, 0], [0, 0, -1, 0], [0, 0, 0, 1]])
write_point_cloud(str(file)+".pcd", pcd)

## Slide 7
RGB Image
Depth Image
Point Cloud

## Slide 8: Object detection using ROS-PCL
Point cloud data
ROS-PCL
Downsampling
Euclidean clustering
Segmentation

## Slide 9: Data-Acquisition using Kinect
Indoor Hostel Environment
Kinect Studio
Capture depth point cloud video
frames

## Slide 10
Testing Using ROS
(D3QNTesting.py)
Dataset Kinect Sequence V2
Gazebo Simulator World
FRCN (For Depth Prediction Network)
D3QN(Training)
(D3QNTraining.py)
Reinforcement Learning FlowChart

## Slide 11
Reference from “Towards Monocular Vision based obstacle Avoidance through Deep Reinforcement Learning” Paper

## Slide 12: Conclusion
We have used D3QN based algorithm for obstacle avoidance using RGBD image as input.
The training is done in a simulated environment.
The work done in the project can be used to predict actions in a real environment too.
In the future, the project can be extended to use other reinforcement learning algorithms. Also, currently, the project works well in indoor scenes, which can be further extended for global navigation.